## Slide 1
Autonomous Navigation
Based on
2-Point Correspondence
using ROS
Submitted By: Li-tal Kupperman, Ran Breuer
Advisor: Majd Srour, Prof. Ehud Rivlin
Intelligence Systems Laboratory, CS, Technion.

## Slide 2
The Problem
Robot navigation to a given target using only visual tools, in an unknown indoor planar environment.
The target is given as an image, taken from the target pose.

## Slide 3
The Method
At each step, a picture is captured from the current position of the robot.
The new picture is being compared to the target picture.
The Algorithm computes the rotation and translation to the target pose

## Slide 4
What Makes it So Unique
We use a special structure of the Essential Matrix for a planar scene.
Using only 2-point correspondence
Precision and numerical stability

## Slide 5
Our Components

## Slide 6
Background
Epipolar Geometry
  Epipolar Point
  Epipolar Line
Homography
Essential Matrix

## Slide 7
Epipolar Geometry

## Slide 8
Center Of Projection

## Slide 9
Epipolar Point

## Slide 10
Epipolar Lines

## Slide 11
Homography
3x3 matrix.
Describes the relation between a plane and an image of the plane.
One image – Warping and rotating the image, to be correlated with the plane.
Two images – Describes how 2 images are related to one another, by mapping epipolar lines.

## Slide 12
Essential Matrix
3x3 matrix.
Relates corresponding points in two images.
Calibrated version of the Fundamental matrix.
, where P ’,P are two points in the images.
Useful for determining the translation and rotation between two images.
The rotation matrix can be fully recovered.
Translation up to a scale

## Slide 13
Movement is limited to plane
Rotation around Y axis only
Rotation matrix & Translation vector -
Essential Matrix in Planar Model

## Slide 14
Essential Matrix in Planar Model
Where and
We reduce the essential matrix to this structure

## Slide 15
Algorithm & Implementation

## Slide 16
Program Workflow
  Input : Target image.
  Capture an image from the current pose.
  Extract and match features from both images.
  Filter the largest inliers set using PROSAC.
  Using the best model estimated, extract matrices R and T.
  Calculate the distance to target.
  Move to a new pose and repeat step 1 until target pose is reached.

## Slide 17
Finding a good starting point –
  Scanning and covering 360° of the room.
Finding correspondence –
  Using SIFT method and Brute force matching
  Eliminate bad matches
Starting position & correspondence

## Slide 18
Estimating E
Estimating the Essential Matrix
  Only 2 point correspondence to estimate E.
  Using a variation of PROSAC.
  Finding the largest inlier set that agree with E.

## Slide 19
Estimating E (Cont.)
Estimating the Essential Matrix (cont.)
  Linear equation matrix Ax = 0:
  Where
  Constrained version

## Slide 20
Estimating E (Cont.)
Estimating the Essential Matrix (cont.)
  Unit circle and ellipse intersection
  Using SVD.
  Possible results:
    2 (or 4) intersection points - use for our E.
    No intersection points – no solution.
    Infinite number of points – Pure Rotation.

## Slide 21
What’s the next step?
Pure Rotation –
  Robot at target, but wrong orientation.
Calculating Distance
  With the help of a third image.
  2 Methods implemented:
    Triangle
    Cross ratio

## Slide 22
Design and Implementation
Using ROS nodes to communicate between modules, the robot and the camera.
Auto Navigator – main module.
Robot Controller
Image Capturer + Undistorted
Epipolar Solver

## Slide 23
Auto Navigator Interface Diagram

## Slide 24
Using ROS
Based on Nodes – services.
  subscribe or publish from\to a Topic.
ROSARIA – controlling the robot.
Axis Camera – photo stream, capturing images.

## Slide 25
Challenges
Eliminating bad images
Algorithm divergence near target (Triangle method)
Computing distance to target
Restarting after bad step
Algorithm troubles with a dominant plane

## Slide 26
Experimental Test Results
Convergence : 3-8 iterations, 1-20cm from target.
Triangle method algorithm diverges when close to target.
Comparing distance calculation method

## Slide 28
Target Image

## Slide 29
Starting Position

## Slide 30
Midway – 2nd iteration

## Slide 31
The End

## Slide 32
Target VS. The End
Target
End

## Slide 33
Measurables
Distance to target by iterations

## Slide 34
Measurables
Difference in orientation

## Slide 35
Summary
Vision based navigation can deduce orientation and distance using:
  Feature matching
  Essential Matrix
Planar movement
  Unique Essential Matrix structure.
2-point correspondence.
The algorithm quickly converges close to the target – pose + orientation.

## Slide 36
Future Work
Solving divergence at target pose.
Better elimination of “bad” image sources (wrong poses).
Qualifier for better matches and features for a more efficient estimation each step.
Solve issue with dominant plane scene