## Slide 1: LANDING Extracting Angles From an Image
Submitted by: Li-tal Kupperman, Ziv Nachum
Advisors: Yair Atzmon, Aram Movsisian
Center for Intelligent System, CS, Technion
July 2015

## Slide 2: The Main Goal
The Master project:
  Land a quadcopter on a moving target
Our part:
  Extract angles from an image
  Using data from image stream

## Slide 3: Recognizing the target
  Hough Transform
  First (unsuccessful) trial
  Unable to detect ellipses… only rounded circles.

## Slide 4: Recognizing the target
  Detection Heuristics
  Comparing areas of ellipses and corresponding rectangles.
  Acquire a set of different ellipses. (no repetitions)
  Choosing only the relevant ellipses, according to our target.

## Slide 5: Choosing the target
  First Target
  Problem: Difficult to distinct the actual target from other objects.
  Apparently not as unique as we thought…

## Slide 6: Choosing the target
  Second Target
  Looking for 6 circles, in a certain formation.
  Easier to detect…
  Problem: The target is too symmetrical.
  Unable to decide on the direction the camera was facing.
  Unstable results.

## Slide 7: Choosing the target
  Final Target
  Looking for 7 circles, in a certain formation.
  Easier to detect…
  The extra circle allows to decide on a specific order.
  Led to stabilized results.
  Matches the direction of the camera in the real world.

## Slide 8: Extracting The Angles
Using two sets of points:
  Points in the 2D image plane
    Ellipses in the frame
  Points in the real 3D world
    The real target

## Slide 9: Extracting The Angles
Using Perspective-n-Points:
  Estimate camera pose from given n 3D points and their projection in an image.
  solvePnP function.
  Output:
    Rotation vector
    Translation vector
  Represents the position on the camera with regards to the real world

## Slide 10: Extracting The Angles
Converting the rotation vector, into a rotation matrix
  Rodrigues function
Easier to calculate the angles from a matrix.
Extracting the angles using a given calculation
  As shown in the next slide

## Slide 11: Extracting The Angles

## Slide 12: Final Results
3 angles, representing 3 axes.
Final results displayed in degrees.
Using there 3 angles it is possible to determine the quadcopter’s next move towards the target

## Slide 13: Examples
X: 17.4068, Y:6.23963, Z:-80.3897

## Slide 14: Examples
X: 25.249, Y:-8.4599, Z:57.6348

## Slide 15: Examples
X: 72.1469, Y:-2.32951, Z:-115.046